## Slide 1: Multi-Paths Concurrent Measurement Protocol
draft-dang-ippm-multiple-path-measurement-01
Joanna Dang dangjuanna@huawei.com,
Jianglong Wang wangjl1.bri@chinatelecom.cn

## Slide 2: Overview
Charter for IPPM WG: produced protocols for communication among test equipment to enable the measurement.
Multiple Path Measurement [draft-dang-ippm-multiple-path-measurement-01] is mainly in concurrently measuring the multiple paths in equal-cost multi-path (ECMP) or unequal-cost multiple (UCMP) scenarios.

## Slide 3: Multiple Paths
A
B
N1
N2
N4
N3
N6
N5
Has a definite Src node and Dst node
Be Adopted in the equal-cost multi-path (ECMP) or unequal-cost multiple (UCMP) scenarios
Each path of the multiple path are unidirectional.
Path1: A->N1->N2->B
Path2: A->N3->N4->B
Paht3: A->N5->N5->B
Src node
Dst node

## Slide 4: Motivation
Path1: A->N1->N2->B
Path2: A->N3->N4->B
Paht3: A->N5->N5->B
Senario1: The services with different quality requirements is imported to the available paths on demand.
Senario2: There is a path congestion. The part of traffic causing the path congestion is adjusted to other light loads.
Challenge: Each path is measured separately in traditional method. If you want to ensure that the data obtained by the test is available and accurate, the test start point and end point in multiple paths must be consistent.
Solution: The Multi-Path Concurrent Measurement Protocol (MPCMP) is required.
A
B
N1
N2
N4
N3
N6
N5
Service1
Service2
Service3
Src node
Dst node
A
B
N1
N2
N4
N3
N6
N5
Service1
Src node
Dst node
Figure1: Senario1
Figure2: Senario1
Notes: TSN 致力于一个converged network，就是承载 需要确定性低时延的流和BE流。。

## Slide 5: Multi-Path Concurrent Measurement Protocol
Session ID: A set of multiple paths
Path ID: One path of the session.
Flags: Identify the query or response type.
A
B
N1
N2
N4
N3
N6
N5
Src node
Dst node
Query message in Path1
Query message in Path2
Query message in Path3
Response message
with Path1, path2 and path3 measurement info
The sender generate a multipath measurement at the same time.
  Each path has its own query message.
Get the quality data of a multipath measurement at the same time through any path
  The measurement results at the receiver can be sent back or sent in a sesponse message because the main consideration is to save network bandwidth.
Receiver
Sender

## Slide 6: Measurement Mode
Long-term measurement
  The receiver can wait until it receives all measurement requests of a set of path and then responds.
Short-term measurement
  The sender can query once t.
  The receiver can reply once t.
When the period is shorter, the measurement accuracy is higher.
Src node
Dst node
Tmax
Src node
Dst node
Tmax
P
1
P
2
P
3
P
1
P
2
P
3
P
1
P
2
P
3
P
1
P
2
P
3
Receiver
Sender
Notes: TSN 致力于一个converged network，就是承载 需要确定性低时延的流和BE流。。

## Slide 7: Next Step
Think deeply in conjunction with Segment Routing Policy and In-situ OAM (IOAM) scenarios

## Slide 8: Thank you!