## Slide 1: Path Congestion Metric
draft-dang-ippm-congestion-01
Joanna Dang dangjuanna@huawei.com,
Jianglong Wang wangjl1.bri@chinatelecom.cn

## Slide 2: Overview
Charter for IPPM WG: define specific metrics and procedures for accurately measuring and documenting these metrics.
Path Congestion Metric [draft-dang-ippm-congestion-01] is mainly measuring E2E path congestion.

## Slide 3: Motivation
A
B
N1
NodeA/NodeC doesn’t sense the congestion between node N2 and Node B.
We don’t know why the congest occurs or which path the congestion affects.
N2
Congestion
C
N3
Two Path
  Path1: A->N1->N2->B
  Path2: C->N3->N2->B
Path Congestion Metric is required.
If path1 is congested by measurement, nodeA will adapted part of the traffic to relief the congestion between N2 and B.
If path2 is congested by measurement, nodeC will adapted part of the traffic to relief the congestion between N2 and B.
As a result, the congestion will be avoided and the service experience in path1 and path2 will also be guaranteed.

## Slide 4: Path
A
B
N1
N2
Dst Node
Src Node
A path： A->N1->N2->B
Has a definite Src node and Dst Node
A path of multiple paths in the equal-cost multi-path (ECMP) or unequal-cost multiple (UCMP) scenarios
Be unidirectional
  Statistics on the number of packets at the Src node and the Dst node
  One-way delay measurement

## Slide 5: Path Congestion Metric
There are 3 scenarios about path congestion metric.
No packet loss occurs, path congestion metric is
  0 when there is no path congestion.
      Path Delay = (Propagation Delay + Transmission Delay)
      In one cycle, the number of packets received by the Dst is the same as sent packets by the Src.
  >0 when the path is congested.
      Path Delay = (Propagation Delay + Transmission Delay + Path Queue Delay)
      In one cycle, the number of packets received by the Dst is less than sent packets by the Src.
When packet loss occurs, packet loss is more serious than congestion. Therefore, the packet loss problem is solved first and then the path congestion metric is monitored.

## Slide 6: Methodologies for a Type-P-Path-Congestion Metric
Sequences of measurement messages
Path latency of measurement messages
S1
S2
dpt
t1
min{Path Delay}
dpt
t4
t2
dpt
t8
Path Queue Delay
Path Congestion Metric
t3
dpt
dpt
t9
t6
t5
t7
Path traffic rate
Tmax
Congestion
Path Congestion Metric
Short-term measurement
Although not receiving the second measurement packet, but the number of service traffic packets reached at Dst is periodically counted after receiving the first measurement packet.
Long-term measurement
The Dst receives the second measurement packet.
When the period is shorter, the measurement accuracy is higher.

## Slide 7: Methodologies for Samples of Path Congestion
Sequences of measurement messages
Path traffic rate
Path latency of measurement messages
Tmax
S1
S2
S3
S4
S5
S6
Path Congestion Metric
dpt
dpt
dpt
dpt
dpt
dpt
dpt
dpt
dpt
dpt
t4
t2
t1
t3
dpt
t5
t6
t7
t9
dpt
Path Queue Delay
min{Path Delay}
Congestion
Packet Loss
Congestion
t8
Path Congestion Metric
Short-term measurement
Long-term measurement

## Slide 8: Next Step
Think deeply in conjunction with In-situ OAM (IOAM) and Segment Routing Version6 (SRv6) scenarios
Make congestion adjustment and avoidance

## Slide 9: Thank you!