## Slide 1: Simple Two-way Active Measurement Protocol (STAMP) Extensions draft-mirsky-ippm-stamp-option-tlv
Greg Mirsky gregimirsky@gmail.com Richard Foote, footer.foote@nokia.com
Guo Jun guo.jun2@zte.com.cn Xiao Min xiao.min2@zte.com.cn
Henrik Nydell hnydell@accedian.com
IETF-104 March 2019, Prague

## Slide 2: Updates to STAMP Extensions
Originally, Section 5 TLV Extensions to STAMP of draft-ietf-ippm-stamp, spawned as separate draft
Type values less than 32768 identify mandatory TLVs that MUST be supported by an implementation. Type values greater than or equal to 32768 identify optional TLVs that SHOULD be ignored if the implementation does not understand or support them. If a Type value for TLV or sub-TLV is in the range for Vendor Private Use, the Length MUST be at least 4, and the first four octets MUST be that vendor's the Structure of Management Information Private Enterprise Number, in network octet order. The rest of the Value field is private to the vendor.
The use of extension TLVs is at the discretion of a Session-Sender. A Session-Sender may use some TLVs intermittently. For example, Timestamp TLV may be used at the start of the STAMP session or periodically, e.g., once an hour, day or week. The same applies to Location TLV. On the other hand, Class of Service TLV may be present in every test packet either to monitor consistency of CoS behavior along the path or to test the CoS behavior.
IANA Considerations

## Slide 3: Extra Padding TLV
The Extra Padding TLV is similar to the Packet Padding field in TWAMP-Test packet [RFC5357]. In STAMP the Packet Padding field is used to ensure symmetrical size between Session-Sender and Session-Reflector test packets. Extra Padding TLV MUST be used to create STAMP test packets of larger size.

## Slide 4: Location TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Location Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source MAC |
+ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| | Reserved A |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Destination IP Address ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Source IP Address ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Dest.port | Src.Port | Reserved B |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
The Location TLV MAY be used to determine the last-hop addressing for STAMP packets including source and destination IP addresses as well as the MAC address of the last-hop router. Last-hop MAC address MAY be monitored by the Session-Sender whether there has been a path switch on the last hop, closest to the Session-Reflector. The IP addresses and UDP port will indicate if there is a NAT router on the path, and allows the Session-Sender to identify the IP address of the Session-Reflector behind the NAT, detect changes in the NAT mapping that could cause sending the STAMP packets to the wrong Session-Reflector.

## Slide 5: Timestamp TLV
Sync Src In/Sync Src Out - one octet long field that characterizes the source of clock synchronization at the ingress and egress of Session-Reflector. There are several of methods to synchronize the clock, e.g., Network Time Protocol (NTP) [RFC5905], Precision Time Protocol (PTP) [IEEE.1588.2008], Synchronization Supply Unit (SSU) or Building Integrated Timing Supply (BITS), or Global Positioning System (GPS), Global Orbiting Navigation Satellite System (GLONASS) and Long Range Navigation System Version C (LORAN-C).
Timestamp In/Timestamp Out - one octet long field that characterizes the method by which the ingress of Session-Reflector obtained the timestamp T2 and T3 respectively. A timestamp may be obtained with hardware assist, via software API from a local wall clock, or from a remote clock (the latter referred to as "control plane").
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp Information Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sync. Src In | Timestamp In | Sync. Src Out | Timestamp Out |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 6: Class of Service TLV
DSCP1 - The Differentiated Services Code Point (DSCP) intended by the Session-Sender. To be used as the return DSCP from the Session-Reflector.
DSCP2 - The received value in the DSCP field at the Session- Reflector in the forward direction.
ECN - The received value in the ECN field at the Session-Reflector in the forward direction.
Reserved - 18 bits long field, must be zeroed in transmission and ignored on receipt.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Class of Service Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DSCP1 | DSCP2 |ECN| Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: Next steps
Comments are welcome
Ask for WG adoption

## Slide 8: Extending Active Measurement Protocol
RFC 8545 in Section 4 stated:
  For avoidance of doubt, the implementation of both TWAMP-Control and TWAMP-Test is REQUIRED for Standards Track TWAMP as specified in [RFC5357].
STAMP:
  use STAMP Extension TLVs;
  augment STAMP YANG model.