## Slide 1: Performance Measurement in Segment Routing Networks with MPLS Data Plane
draft-gandhi-spring-sr-mpls-pm-03
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Stefano Salsano - Universita di Roma "Tor Vergata" (stefano.salsano@uniroma2.it)
Pier Luigi Ventre - CNIT (pierluigi.ventre@cnit.it)
Mach Chen - Huawei (mach.chen@huawei.com)
Sagar Soni - Cisco Systems (sagsoni@cisco.com)
Patrick Khordoc - Cisco Systems (pkhordoc@cisco.com)
Zafar Ali - Cisco Systems (zali@cisco.com)
Daniel Bernier - Bell Canada (daniel.bernier@bell.ca)

## Slide 2: Agenda
Requirements and Scope
In-band Probes for SR Links and P2P and P2MP SR Policies
DM and LM Packets for SR Links and SR Policies
Probe Responses
Path Segment ID for PM
SR Link Extended TE Metrics Advertisements
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM) for SR links and end-to-end P2P and P2MP SR Policies
  Delay and Loss extended TE link metrics advertisement in the network
  Scope:
    Segment Routing (SR) with MPLS data plane
    In-band PM probe messages
    Use RFC 6374 (defined for MPLS-TP) based mechanisms
    Use RFC 7876 (UDP return path) for probe response messages
    Informational

## Slide 4: PM Probes for SR Links
For SR links, the PM probe query messages for link delay and packet loss measurements are sent in-band using MPLS GAL/GAch header as defined in [RFC6374].

## Slide 5: PM Probes for P2P and P2MP SR Policies
For end-to-end measurement of P2P and P2MP SR Policies, the PM probe query messages for delay and loss measurements are sent in-band using MPLS GAL/GAch header as defined in [RFC6374] and SR-MPLS label stack.

## Slide 6: DM Probes for SR Links and SR Policies
DM probes use the message format defined in [RFC6374] as payload.
  GAL : 13
  GAch : 0x000C

## Slide 7: LM Probes for SR Links and SR Policies
LM probes use the message format defined in [RFC6374] as payload.
  GAL : 13
  GAch : 0x000A (Direct mode)
  0x000B (Inferred mode)

## Slide 8: Probe Responses
One-way Measurement Response (out-of-band)
  Sent to the querier node using the information from the UDP Return Object (URO) TLV [RFC7876].
  URO TLV is sent by the querier node in the probe query messages and contains the UDP destination port and IP address.
Two-way Measurement Response (in-band)
  Sent to the querier node using a message similar to the in-band probe query message as SR-MPLS packet.

## Slide 9: Path Segment ID
Path Segment IDs [draft-cheng-spring-mpls-path-segment] are useful for Performance Measurement:
  Loss Measurement
  Bidirectional SR Policy

## Slide 10: SR Link Extended TE Metrics Advertisement
PM procedure is used to measure delay and loss performance of SR Links.
Compute SR Link Delay metrics (minimum-delay, maximum-delay, average-delay, delay-variance) and SR Link Packet Loss metric.
SR link extended TE metrics advertised in the network using the TLVs defined in the following RFCs/Drafts:
  OSPF [RFC7471]
  ISIS [RFC7810] [draft-ietf-lsr-isis-rfc7810bis]
  BGP-LS [draft-ietf-idr-te-pm-bgp]

## Slide 11: Next Steps
Welcome your comments and suggestions
Multiple implementations already exist
Request for WG adoption

## Slide 12
Thank you.