## Slide 1: M-PDM
draft-fear-ippm-mpdm-03
Nalini Elkins, Giuseppe Fioccola, Mike Ackermann, Rob Hamilton
IETF 103
November 18, 2018

## Slide 2: Combines PDM and Marking
RFC8250 : Performance and Diagnostic Metrics (PDM)
RFC8321: Alternate-Marking Method for Passive and Hybrid Performance Monitoring

## Slide 3: Why?
PDM : IPv6 Destination Option provides packet sequence number and performance information end-to-end
Marking provides error information
Marking is IPv4 only
Need one-way network path information as well as end-to-end metrics

## Slide 4: PDM Fields
Performance and Diagnostic Metrics Destination Option (PDM) contains the following fields: (by 5-tuple)
PSNTP : Packet Sequence Number This Packet
PSNLR : Packet Sequence Number Last Received
DELTATLR : Delta Time Last Received
DELTATLS : Delta Time Last Sent
SCALEDTDL : Scale for Delta Time Last Received
SCALEDTLS : Scale for Delta Time Last Sent

## Slide 5: PDM Provides:
Round trip delay
Server delay
Does not provide one-way delay or middlebox delay

## Slide 6: M-PDM HBH Header
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option Type | Option Length |Version|LastM |M | MType |Rsvd |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Middlebox Identifier | Timestamp In |
|-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp Out | PSN This Packet |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
--- [Room for 5 middleboxes ]
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Middlebox Identifier | Timestamp In |
|-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp Out | PSN This Packet |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Fixed length header
Sent by source
Each middlebox will update
More than 5 will wrap
LastM is Last Middlebox who updated.

## Slide 7: Timestamp Calculation
16 bits
Delta from fixed offset
January 1, 2019
Same calculation as PDM

## Slide 8: Next Steps / Questions
What should Middlebox identifier be?
Collaborate with iOAM work? Inside an administrative domain?
Comments?