## Slide 1: Enhanced Alternate Marking Method
draft-zhou-ippm-enhanced-alternate-marking-00
Tianran Zhou
Giuseppe Fioccola
Haoyu Song
Zhenbin Li
Huawei
Zhenqiang Li
China Mobile

## Slide 2
Motivation
Alternate Marking (RFC8321) is technique is an hybrid performance measurement method.
  It can be used to measure packet loss, latency, and jitter on live traffic.
  The basic Alternate Marking method requires one or two bits to mark consecutive batches of packets.
However
  In some protocols, no additional bit can be used
  Limited by the scalability for further extension

## Slide 3
Basic Ideas
Two kinds of measurement:
Flow ID: help to identify the measured flow.
More reserved field for further use.
Delay, packet loss
End to end
Delay, packet loss
Hop by hop

## Slide 4
where:
L - Loss flag;
D - Delay flag;
FlowID - 6-octet unsigned integer. Flow identifier field is to uniquely identify a monitored flow within the in-situ OAM domain.
Encapsulate with the End to End IOAM
IOAM [I-D.ietf-ippm-ioam-data] defines a generic meta data structure to records OAM information within user packets while the packets traverse a network.
The IOAM-E2E-Type filed within the IOAM edge-to-edge option header is a 16-bit identifier which specifies which data types are used in the E2E option data.
One bit from bit 4-15 can be used to indicate the presence of data used for alternate marking.

## Slide 5
Encapsulate with the PostCard Base Telemetry
The PostCard Base Telemetry (PBT) [I-D.song-ippm-postcard-based-telemetry] is proposed to directly exports the telemetry data to a collector through separated OAM packets called postcards, while not require inserting telemetry data into user packets.
This proposes to use the two bits from the Reserved field from the Telemetry Information Header (TIH).
The existing FlowID within the TIH can be reused.
where:
L - Loss flag;
D - Delay flag.

## Slide 6: Thank You and Comments